## Slide 1: Standard file format for the exchange of gridded geodetic data
Roger Lott, Melita Kennedy
International Association of Oil & Gas Producers (IOGP)
Geodesy Subcommittee
Kevin Kelly, Rob Juergens, David Burrows, Keith Ryden
Esri

## Slide 2: What is the issue?
Use of gridded data in geodesy is increasing
  More lat-long offset grids
  More geoid and height correction models
  More velocity and deformation grids
Trend expected to continue
No standard file format exists
  Different organizations use different formats for the same data type
    NADCON, NTv2
  Multiple formats even within the same creating organization
    EGM96, EGM2008
  Each geodetic data type has its own grid format

## Slide 3: What is the problem?
Because each grid is in a different format, developers of globally-marketed applications have had to repeatedly write code to import the different grids.
EPSG defines a different coordinate operation method for each geoid file format
Users of globally-marketed applications have been unable to use the gridded data until it has been incorporated into the application they use.
Many existing formats do not define what the data represents

## Slide 4: What are the benefits?
Grid producers would not have to provide reading software for their data.
Geodesy, survey and GIS software developers would need to read only one grid file format.
End users could use a new grid file in their application as soon as it became available, without having to wait for their vendor to produce a software upgrade.

## Slide 5: Characteristics of a standard geodetic grid data exchange file format
Support multi-resolution data through nested sub-grids
Support multi-dimensional data
Informative header
  Including description fields to identify the data
User-definable content
  Using KEYWORDS for standard datatypes
Fast access to any part of potentially large files
Support ASCII and Binary files
Open-source file IO library in modern development languages
  Code to read and write grids
  Code to convert between ASCIIBinary
Published and versionable standard file syntax
  So users can write their own code if desired
Extendable format

## Slide 6: Why not NetCDF, HDF, etc?
No published, documented format syntax
Dependence on third-party code libraries
  Vendor restrictions may prevent using these
  Libraries may not exist on all platforms
Not platform independent
  iOS, Android NetCDF API does not exist
  Cannot depend on third parties to write API’s
No control over the performance
Interoperability issues
Formidable learning curve to use
Few geodetic agencies actually use

## Slide 7: What this is not
There is no intention of producing a generic, self defining, extensible, grid file format.
  too complex
  complexity would limit adoption
Proposal is to limit the scope to geodetic data
  this allows explicit description of contents

## Slide 8: OGC and/or ISO Standard?
Success will be determined by adoption
Having an ISO standard might help adoption in some governmental organisations creating gridded geodetic data
CRS Well Known Text was done as a joint OGC/ISO project, and that seemed to work well

## Slide 9: So what‘s next?
Set up a WIKI to document under the CRS Domain Working Group
  Upload initial material that has been gathered
  Define requirements and project scope
Determine if there is interest – we’d need people interested in different aspects of the project:
  Requirements and Design
  Specification writing
  Open Source API implementation
  Testing
Draft a SWG charter for review